## Slide 1: ROSE-T: Making MANRS Compliance Simple (And Automatic!)
Mariano Scazzariello *, Antonio Prado †, Tommaso Caiazzi ‡,
* KTH Royal Institute of Technology, Sweden
† “G. D’Annunzio” University, Italy ‡ Roma Tre University, Italy

## Slide 2: Why is Routing Security Crucial Nowadays?
Cyber Threats
Business Continuity
Sensitive Data
Notes: We all know that routing security is at foremost importance nowadays.

## Slide 3: Why is Routing Security Crucial Nowadays?
Cyber Threats
Business Continuity
Sensitive Data
Notes: And MANRS initiative is playing a key role in making the Internet a safer place.

## Slide 4: MANRS Guidelines For Network Operators
Coordination
Network operators maintain globally accessible up-to-date contact information
Global Information
Network operators must publicly document their routing policies, ASNs and prefixes
Anti-Spoofing
Prevent packets with spoofed source IP address from entering or leaving the network
Filtering
Prevent propagation of incorrect routing information
Notes: In this talk we focus on the MANRS Network Operators guidelines. We know that Coordination, Global Information, Anti-Spoofing and Filtering are the four actions that a network operator must perform to verify MANRS compliance.

## Slide 5: MANRS Guidelines For Network Operators
Coordination
Network operators maintain globally accessible up-to-date contact information
Global Validation
Network operators must publicly document their routing policies, ASNs and prefixes
Anti-Spoofing
Prevent packets with spoofed source IP address from entering or leaving the network
Filtering
Prevent propagation of incorrect routing information
How Can a Network Operator Ensure the MANRS Compliance?
Notes: After reading them, we ask: ok, let’s assume I’m an operator and I want to ensure that my network is MANRS compliant. How can I verify so?

## Slide 6: How Can a Network Operator Ensure the MANRS Compliance?
Coordination
Global Validation
Anti-Spoofing
No tool to automatically verify MANRS compliance!
Operators have to check their configurations and routing policies manually or with minimal aid
Not an easy task!
Filtering
Limited reproducibility of the process
Notes: The reality is that there is no tool to automatically verify MANRS compliance.
> So, the validation is a cumbersome process for operators, that have to manually check configurations and policies.
>And this also makes difficult to replicate the process if needed.
>So yes, while ensuring MANRS compliance is crucial, it becomes a difficult task to achieve!

## Slide 7: ROSE-T: ROuting SEcurity Tool
Parse the Configuration
Understand Vendor-specific Language
Analyze the Configuration
Reconstruct the Neighbours Relationships
Emulate the Minimal Network Topology
Behave as Close as Possible to the Real One
Verify “Anti-Spoofing” and “Filtering”
On the Emulated Network
Gather Candidate Information
Verify Their Correctness for “Global Information”
The first open-source tool to automatically verify MANRS compliance
Trust No One approach
Run ROSE-T locally to perform the self-assessment of the configuration
Notes: To address this problem, in this talk I will briefly present ROSE-T, the first open-source tool to automatically verify MANRS compliance.

## Slide 8: ROSE-T – Step-by-Step
Parse
Analyze
Emulate
Verify
Gather
Notes: Let’s take a brief look to the process

## Slide 9: ROSE-T – Step-by-Step
Parse
Analyze
Emulate
Verify
Gather Candidate Information
Verify Their Correctness for “Global Information”
IRR Entry
RPSLng
RIB Dump
Routes originated by candidate AS
Verify that the networks announced to transits are in the IRR Entry
Verify that the networks in the IRR Entry are announced to transits
Notes: First, the candidate provides the AS number.
From this, >we can fetch the IRR entry and parse the aut-num objects. For now, we manually parse the RPSLang syntax, but in the future we plan to rely on better services such as IRRd.
>We also take the latest RIB Dump from a RouteCollector, and from this >we can filter the routes originated by the candidate by checking their AS_PATH.
>We then use Prolog to verify that the set of networks announced to the transits «in the wild» is equal to the ones defined in the IRR entry, and viceversa.
For now, we only focus on the transits, but we plan to extend the verification to all the peerings.

## Slide 10: ROSE-T – Step-by-Step
Parse the Configuration
Understand Vendor-specific Language
Analyze
Emulate
Verify
Gather
Vendor-specific Configuration
AS C
AS B
AS D
AS A
Agnostic Format
Exploit what Batfish does best: parsing vendor configurations
Notes: At this point we can take the vendor-specific configuration. >And we need to transform it into an agnostic format that can be easily processed in the rest of the pipeline.
>How can we do that?
>In ROSE-T we exploit Batfish, since it’s able to understand most of the vendor syntaxes and translate them into a unified format.

## Slide 11: ROSE-T – Step-by-Step
Parse the Configuration
Understand Vendor-specific Language
Analyze
Emulate
Verify
Gather
Vendor-specific Configuration
AS C
AS B
AS D
AS A
Agnostic Format
Exploit what Batfish does best: parsing vendor configurations
Enrich it with missing information
Take Batfish’s output as a foundation
Notes: We noticed that Batfish lacks of some important features. For example, currently it doesn’t support IPv6.
So we use the Batfish output as a baseline, >and we extract the missing information using another custom parser that we wrote.
Of course, to fast iterate on the project we used Batfish, but in the future we want to write our own parser.

## Slide 12: ROSE-T – Step-by-Step
Analyze the Configuration
Reconstruct the Neighbours Relationships
Emulate
Verify
Gather
Parse
AS B
AS C
AS D
AS A
Agnostic Format
Notes: Ok now we have a datastructure holding the essential information into an agnostic format.

## Slide 13: ROSE-T – Step-by-Step
Analyze the Configuration
Reconstruct the Neighbours Relationships
Emulate
Verify
Gather
Parse
AS B
AS C
AS D
AS A
Agnostic Format
What are their relationships?
IRR Entry
RPSLng
Notes: But we don’t know the relationships between the ASes. >So, we again rely on the IRR entry to set the relationships.

## Slide 14: ROSE-T – Step-by-Step
Analyze the Configuration
Reconstruct the Neighbours Relationships
Emulate
Verify
Gather
Parse
Intermediate Representation
IRR Entry
RPSLng
AS B
AS C
AS D
AS A

## Slide 15: ROSE-T – Step-by-Step
Analyze the Configuration
Reconstruct the Neighbours Relationships
Emulate
Verify
Gather
Parse
Intermediate Representation
IRR Entry
RPSLng
AS B
AS C
AS D
AS A
«Internet»
Dummy OTT connected to all providers
Notes: For being consistent with a realistic network, we plug a dummy OTT connected to all providers.

## Slide 16: ROSE-T – Step-by-Step
Analyze the Configuration
Reconstruct the Neighbours Relationships
Emulate
Verify
Gather
Parse
RIB Dump
Intermediate Representation
AS B
AS C
AS D
AS A
«Internet»
AS B Routes
AS C Routes
AS D Routes
0.0.0.0/0
::/0
ROSE-T also supports multi-hop peerings!
Notes: Now, we again use the RIB Dump and we add the prefixes originated by each AS.
>This example only shows how direct peerings are interpreted by ROSE-T, but we also support multi-hop peerings with a slightly complex logic.

## Slide 17: ROSE-T – Step-by-Step
Emulate the Minimal Network Topology
Behave as Close as Possible to the Real One
Verify
Gather
Parse
Analyze
Intermediate Representation
AS B
AS C
AS D
AS A
«Internet»
AS B Routes
AS C Routes
AS D Routes
0.0.0.0/0
::/0
Notes: At this point we transform this intermediate representation into a runnable network scenario.

## Slide 18: ROSE-T – Step-by-Step
Emulate the Minimal Network Topology
Behave as Close as Possible to the Real One
Verify
Gather
Parse
Analyze
Intermediate Representation
AS B
AS C
AS D
AS A
«Internet»
AS B Routes
AS C Routes
AS D Routes
0.0.0.0/0
::/0
Notes: To run the emulation, we rely on Kathara, an open-source network emulator based on containers.

## Slide 19: ROSE-T – Step-by-Step
Emulate the Minimal Network Topology
Behave as Close as Possible to the Real One
Verify
Gather
Parse
Analyze
Runnable Network Scenario
AS B
AS C
AS D
AS A
«Internet»
Notes: Each AS is then represented with a router.

## Slide 20: ROSE-T – Step-by-Step
Emulate the Minimal Network Topology
Behave as Close as Possible to the Real One
Verify
Gather
Parse
Analyze
Runnable Network Scenario
AS B
AS C
AS D
AS A
«Internet»
Vendor Container
More to come…
ROSE-T can easily be extended to support other vendors
Notes: For all the routers except the candidate one, we use FRRouting as the routing suite.
>As for the candidate router, we use the specific vendor container that it’s derived from the configuration. For now we support Cisco IOS-XR and JunOS, but >the tool can easily be extended to support other vendors.

## Slide 21: ROSE-T – Step-by-Step
Verify “Anti-Spoofing” and “Filtering”
On the Emulated Network
Gather
Parse
Analyze
Emulate
AS B
AS C
AS D
AS A
«Internet»
Notes: After waiting for the network convergence, we can start performing the verification. > Let’s add two hosts that will be used to perform the tests.

## Slide 22: ROSE-T – Step-by-Step
Verify “Anti-Spoofing” and “Filtering”
On the Emulated Network
Gather
Parse
Analyze
Emulate
AS B
AS C
AS D
AS A
«Internet»
Anti-Spoofing
Notes: For time reasons, I will only show the Anti-Spoofing check.

## Slide 23: ROSE-T – Step-by-Step
Verify “Anti-Spoofing” and “Filtering”
On the Emulated Network
Gather
Parse
Analyze
Emulate
AS B
AS C
AS D
AS A
«Internet»
Anti-Spoofing
For each Provider:
Notes: So we take the providers and for each one of them

## Slide 24: ROSE-T – Step-by-Step
Verify “Anti-Spoofing” and “Filtering”
On the Emulated Network
Gather
Parse
Analyze
Emulate
AS B
AS C
AS D
AS A
«Internet»
Anti-Spoofing
For each Provider:
Insert a Client
Notes: We insert a client machine inside the same AS.

## Slide 25: ROSE-T – Step-by-Step
Verify “Anti-Spoofing” and “Filtering”
On the Emulated Network
Gather
Parse
Analyze
Emulate
AS B
AS C
AS D
AS A
«Internet»
Anti-Spoofing
For each Provider:
Insert a Client
Assign IPs (v4/v6) to each Client
195.22.194.43
185.5.200.1
Carefully choose subnets that are correctly announced and reachable
Notes: We then assign both IPv4 and IPv6 addresses to each client.
>The challenge here is to choose subnets that are correctly announced and mutually reachable from the information at our disposal.

## Slide 26: ROSE-T – Step-by-Step
Verify “Anti-Spoofing” and “Filtering”
On the Emulated Network
Gather
Parse
Analyze
Emulate
AS B
AS C
AS D
AS A
«Internet»
Anti-Spoofing
For each Provider:
Insert a Client
Assign IPs (v4/v6) to each Client
195.22.194.43
185.5.200.1
Carefully choose subnets that are correctly announced and reachable
Select a non-overlapping network for the “Internet” host
12.11.10.2
Notes: Moreover, another challenge is to select a valid random IP subnet to assign to the internet host, that doesn’t overlap with the other prefixes announced in the network. This subnet will act as the malicious subnet.

## Slide 27: ROSE-T – Step-by-Step
Verify “Anti-Spoofing” and “Filtering”
On the Emulated Network
Gather
Parse
Analyze
Emulate
AS B
AS C
AS D
AS A
«Internet»
Anti-Spoofing
For each Provider:
Insert a Client
Assign IPs (v4/v6) to each Client
195.22.194.43
185.5.200.1
12.11.10.2
Send the spoofed ICMP packet
12.11.10.2
195.22.194.43
DstIP
SrcIP
Spoofed
Notes: Now we perform the actual check.
>We put a tcpdump on the Internet host to sniff packets.
>Using Scapy we craft a ICMP packet from the candidate client host. This will have the spoofed IP as source and the provider client IP as destination.

## Slide 28: ROSE-T – Step-by-Step
Verify “Anti-Spoofing” and “Filtering”
On the Emulated Network
Gather
Parse
Analyze
Emulate
AS B
AS C
AS D
AS A
«Internet»
Anti-Spoofing
For each Provider:
Insert a Client
Assign IPs (v4/v6) to each Client
195.22.194.43
185.5.200.1
12.11.10.2
Send the spoofed ICMP packet
12.11.10.2
195.22.194.43
DstIP
SrcIP
Spoofed
Notes: We send this packet and two conditions can arise. If the packet is forwarded from the candidate router towards the provider,

## Slide 29: ROSE-T – Step-by-Step
Verify “Anti-Spoofing” and “Filtering”
On the Emulated Network
Gather
Parse
Analyze
Emulate
AS B
AS C
AS D
AS A
«Internet»
Anti-Spoofing
For each Provider:
Insert a Client
Assign IPs (v4/v6) to each Client
195.22.194.43
185.5.200.1
12.11.10.2
Send the spoofed ICMP packet
195.22.194.43
12.11.10.2
DstIP
SrcIP
Notes: We check if the packet is received by the internet client

## Slide 30: ROSE-T – Step-by-Step
Verify “Anti-Spoofing” and “Filtering”
On the Emulated Network
Gather
Parse
Analyze
Emulate
AS B
AS C
AS D
AS A
«Internet»
Anti-Spoofing
For each Provider:
Insert a Client
Assign IPs (v4/v6) to each Client
195.22.194.43
185.5.200.1
12.11.10.2
Send the spoofed ICMP packet
195.22.194.43
12.11.10.2
DstIP
SrcIP
The configuration is not compliant!
Notes: If so, it means that the configuration is not compliant.

## Slide 31: ROSE-T – Step-by-Step
Verify “Anti-Spoofing” and “Filtering”
On the Emulated Network
Gather
Parse
Analyze
Emulate
AS B
AS C
AS D
AS A
«Internet»
Anti-Spoofing
For each Provider:
Insert a Client
Assign IPs (v4/v6) to each Client
195.22.194.43
185.5.200.1
12.11.10.2
Send the spoofed ICMP packet
12.11.10.2
195.22.194.43
DstIP
SrcIP
Spoofed
Notes: Instead, if the candidate correctly blocks the packet

## Slide 32: ROSE-T – Step-by-Step
Verify “Anti-Spoofing” and “Filtering”
On the Emulated Network
Gather
Parse
Analyze
Emulate
AS B
AS C
AS D
AS A
«Internet»
Anti-Spoofing
For each Provider:
Insert a Client
Assign IPs (v4/v6) to each Client
195.22.194.43
185.5.200.1
12.11.10.2
Send the spoofed ICMP packet
12.11.10.2
195.22.194.43
DstIP
SrcIP
Spoofed
The configuration is compliant!
Notes: No packet is received by the internet client and the configuration is compliant.
As a double check, we also verify that legit packets are correctly forwarded and received by the provider host.

## Slide 33: Conclusions
The ROSE-T tool:
Implements the first tool to automatically verify MANRS compliance
Allows network operators to test their configurations without relying on manual and error-prone procedures
Reduces the time for MANRS adoption that would lead to a more secure global routing infrastructure
Notes: So, to conclude I briefly presented ROSE-T, >the first tool to automatically verify MANRS compliance.
>ROSE-T allows network operators to finally test their configurations without relying on manual and error-prone procedures
And this will surely help in speeding-up MANRS adoption if the project becomes widespread.

## Slide 34: Future Work
Extend verification to multiple routers
Currently, ROSE-T implements the verification of Network Operators Actions
  Expand the support to IXPs and CDNs Verification
ROSE-T aims to verify networks beyond MANRS…
  Verify RPKI deployments
  Additional features (e.g., ASPA validation)
Release a verifiable code to certify MANRS compliance
Notes: The work is preliminary and surely there is a lot of future work.
>The first step is to extend the verification from a single router to multiple routers, considering also iBGP and IGP.
>We plan to extend the verification to IXPs and CDNs/cloud providers
>Moreover, the tool was born to verify MANRS, but it could be useful for additional purposes, for example verifying the RPKI deployment of the candidate AS, or validate ASPA.
>Another really cool feature could be to release a code, for example a certificate, to have a tangible proof that a certain network is MANRS compliant.

## Slide 35: Contacts
Tommaso Caiazzi
Roma Tre University
Mariano Scazzariello
KTH Royal Institute of Technology
Antonio Prado
“G. D’Annunzio” University
Notes: I am the end, thanks for your attention.
>As I said ROSE-T is an open source tool, you can check more details inside the GitHub repository. We are super happy of any contribution!
Thanks!